- Home

- Markets

- Design Tool

- Contact Us

| Top of Form Bottom of Form |  |
| --- | --- |
| HC785LP-011 Type Motors Product type Johnson Motor PMDC motors Typical markets power & garden tools Typical applications electrical screw drivers Dimensions Ø 42.3 x 67, shaft Ø 5.005 mm Voltage nominal 18 VDC Torque @ constant 8.4 mNm/A Pole number 5 Weight 391 g Email us Downloads Printer friendly version For further technical information, please contact our sales representative in your region. Distribution Your sales & distribution support Stock availability check Dimensions Performance No load Stall Max efficiency Max power Speed (rpm) 21000 - 18400 10500 Current (A) 2.02 101.61 14.32 51.81 Torque (mNm) - 836.49 103.29 418.24 Efficiency (%) - - 77 - Power (W) - - 199.18 406.07 |

- Terms of Use

- Privacy

- Feedback

- JE Website